SWTLLP

# Introduction
SWTLLP (which stands for SFR WiFi Tunnel Logical Link Protocol) is a protocol which works over any lower layer that can ensure frame integrity and determine the frame’s length. Its role is to identify the type of its payload, just like the LLC protocol for 802.11 for example.
# Goals
The only goal of SWTLLP is to carry both the payload and its type. This will allow a SWTP client or server to determine what to do with the payload.
# Assumptions
SWTLLP works over a lower-level protocol that guarantees:
- That the length of a SWTLLP frame can be determined
- That the integrity of a SWTLLP frame is checked
# Implications
A SWTLLP frame has a single field in its header, which is its payload’s type.
# Frame format
Bytes are sent in network order (big-endian)
Every SWTLLP has a single 8-bit header field, that contains its payload type:
Bit	7	6	5	4	3	2	1	0
Data	Payload type

The payload immediately follows the header.
# Payload types
Payload type field value	Payload type
0x00	SWTCP packet
0x01	IPv4 packet
0x02	IPv6 packet
0x03	Compacted IPv4
0x04	Compacted IPv6
0x05	Compacted ICMPv4
0x06	Compacted TCPv4
0x07	Compacted UDPv4
0x08-0xff	Reserved

## SWTCP packet
The SWTCP protocol will not be defined in this document. It is a protocol that is used for SWTP tunnel configuration.
## IPv4 packet
This value indicates that the payload of the SWTLLP frame is an entire IPv4 packet.
## IPv6 packet
This value indicates that the payload of the SWTLLP frame is an entire IPv6 packet.
## Compacted IPv4 packet
This value indicates that the payload of the SWTLLP frame is compacted IPv4 packet. A compacted IPv4 packet is basically an IPv4 packet with a lot of its headers stripped:
Bit	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
+0	Time To Live								Protocol
+16	Destination IP address
+32

We can note here that the IPv4 header’s length was cut from 160 bits to 48 bits, by removing some fields:
- The version field is useless because its value can be determined by the SWTLLP layer.
- The IHL field was removed because we assume that the IP header has a fixed size of 160 bits.
- The DSCP field was removed because QoS will not be used
- The ECN field was removed because we assume that the network link behind the SWTP server will never be congested
- The Total Length field was removed because its value can be determined by the underlying layers
- The identification field was removed because we do not allow fragmentation
- The Flags field was removed because we do not allow fragmentation
- The Fragment Offset field was removed because we do not allow fragmentation
- The Header Checksum field was removed because SWTLLP frames’ integrity is already checked by an underlying protocol
- The Source IP Address field was removed because its value will remain constant over time (the network IP address of the SWTP end point)
- The Options field was removed because we assume that an IPv4 packet has a fixed header length of 160 bits.
## Compacted IPv6 packet
Compacted IPv6 is still to be defined.
## Compacted ICMPv4 packet
## Compacted TCPv4 packet
## Compacted UDPv4 packet